FOSDEM MUSIC BOX – Assembly cheatsheet

1. Resistors:

R2, R3, R8	22R	1/8W 5%	RED-RED-BLACK-GOLD
R1, R6, R7	1.5K	1/8W 5%	BROWN-GREEN-RED-GOLD
R5, R9, R10	10K	1/8W 5%	BROWN-BLACK-ORANGE-GOLD

2. Diodes

D1, D2	1N4148	Warning! Polarity mark is black stripe.

3. IC Sockets

U1	ATTiny85	Warning! Polarity watch the orientation mark.
U2	LM386	Warning! Polarity watch the orientation mark.

The first pin is marked with square pad!

4. Button

RESET	press to PCB

5. Speaker

VERY CAREFUL DO NOT OVERHEAT!
NO more than 3 seconds soldering on pad or you will destroy the speaker.

6. USB Connector	big metal shield pins soldering on bottom!

7. Capacitors

C2, C3	100 nF X5R 50VDC
C1	10 uF 50VDC	insert long pin into circle pad
C4	220 uF 16VDC	insert long pin into circle pad

8. Leds

LED D1	RED	insert long pin into circle pad
POWER	GREEN(clear)	insert long pin into circle pad

9. Light Sensor

R4	10K LDR